## Fire Extinguishers

All vessels with a motor are required to have a Type B fire extinguisher(s) on board if one or more of the following conditions exist:

- Inboard engine

- Vessel length of 26 feet or longer

- Closed compartments where portable fuel tanks may be stored

- Double-bottoms not sealed to the hull or which are not completely filled with flotation material

- Closed living spaces

- Closed storage compartments in which flammable or combustible materials may be stored.

- Permanently installed fuel tanks.

Approved types of fire extinguishers are identified by the following marking on the label—"Marine Type USCG Approved,"—followed by the size and type symbols (B-I or B-II) and the approval number.

Extinguishers should be placed in an accessible area—not near the engine or in a compartment, but where they can be reached immediately. Be sure you know how to operate them and check all extinguishers regularly to make sure they are fully charged.

- Class A extinguishers are for ordinary combustible materials such as paper, wood, cardboard, and most plastics. The numerical rating on these types of extinguishers indicates the amount of water it holds and the amount of fire it can extinguish.

- Class B fires involve flammable or combustible liquids such as gasoline, kerosene, grease and oil. The numerical rating for class B extinguishers indicates the approximate number of square feet of fire it can extinguish.

- Class C fires involve electrical equipment, such as appliances, wiring, circuit breakers and outlets. Never use water to extinguish class C fires - the risk of electrical shock is far too great! Class C extinguishers do not have a numerical rating. The C classification means the extinguishing agent is non-conductive.

- Class D fire extinguishers are commonly found in a chemical laboratory. They are for fires that involve combustible metals, such as magnesium, titanium, potassium and sodium. These types of extinguishers also have no numerical rating, nor are they given a multi-purpose rating - they are designed for class D fires only.

Fire Triangle

# Text boxes

| Fire Extinguisher Requirements |
| --- |
| Classification (type & size) | Foam (minimum gallons) | Carbon Dioxide (minimum pounds) | Dry Chemical (minimum pounds) |
| B-I | 1 1/4 | 4 | 2 |
| B-II | 2 1/2 | 15 | 10 |
| Length Class | Without a Fixed or Permanently Installed System | With a Fixed or Permanently Installed System |
| Less than 26 ft. | one B-I | None |
| 26 ft. to less than 40 ft. | two B-I or one B-II | one B-I |
| 40 ft. to less than 65 ft. | three B-I or one B-II and one B-I | two B-I or one B-II |